## Slide 1: CSCI 2930 Practical System Administration
Lecture 8: Network Infrastructure (continued)

## Slide 2: Layer 1 – Physical Cables
IEEE 802.3 Ethernet defines standards for LANs
Transmission media
  Copper
    Coax
    UTP or (Unshielded) Twisted Pair
    Terminated by RJ-45 connector
    Standard cables labeled by Category…CAT 5/5e, CAT 6, etc
    Categories specify signal speed, pin outs, number of wires…
    Typically only used up to 300ft (100 meters)

## Slide 3: Layer 1 – Physical Cables
  Fiber
    DO NOT BEND PAST 30 DEGREES!
    Multi mode (MM) – Short range LANs and Campus
      Simpler and cheaper
      Changing from LEDs to lasers
      850 nm and 1300 nm wavelength
      OM1 and OM2 use orange jackets while Aqua is recommended for 50/125 µm "laser optimized" OM3 and OM4 fiber
      “Optical Multi-mode”
Notes: LEDs have a maximum modulation rate of 622 Mbit/s because they can not be turned on/off fast enough

## Slide 4: Layer 1 – Physical Cables
MM ISO Classification System
International Organization for Standardization
Transmission Standards | 100 Mb Ethernet | 1 Gb (1000 Mb) Ethernet | 10 Gb Ethernet | 40 Gb Ethernet | 100 Gb Ethernet
OM1 (62.5/125) | up to 2000 meters (FX) | 275 meters (SX) | 33 meters (SR) | Not supported | Not supported
OM2 (50/125) | up to 2000 meters (FX) | 550 meters (SX) | 82 meters (SR) | Not supported | Not supported
OM3 (50/125) | up to 2000 meters (FX) | 550 meters (SX) | 300 meters (SR) | 100 meters | 100 meters
OM4 (50/125) | up to 2000 meters (FX) | 1000 meters (SX) | 550 meters (SR) | 150 meters | 150 meters
Notes: 62.5 core/125nm cladding

## Slide 5: Layer 1 – Physical Cables
    Single mode (SM) – Long Range
      1310 nm or 1550 nm and require more expensive laser sources
      Core diameter between 8 and 10.5 µm and a cladding diameter of 125 µm
      OS1 and OS2 are standard single-mode optical fiber used with wavelengths 1310 nm and 1550 nm (size 9/125 µm)
      Used up to 50 miles or more with standard equipment
Notes: state-of-the-art DWDM optical systems can span thousands of kilometers at 10 Gbit/s, and several hundred kilometers at 40 Gbit/s.

## Slide 6: Layer 1 – Physical Cables
Small form-factor pluggable transceiver SFP/SFP+
  Interface between the network device board and cable
  Obsoletes the old gigabit interface converter (GBIC)
  multi-mode fiber
    SX - 850 nm, for a maximum of 550 m at 1.25 Gbit/s (Gigabit Ethernet) or 150m at 4.25 Gbit/s (Fibre Channel)
  single-mode fiber
    LX - 1310 nm, for distances up to 10 km
    EX - 1310 nm, for distances up to 40 km
    ZX - 1550 nm, for distances up to 80 km
    EZX - 1550 nm, for distances up to 120 km
Notes: state-of-the-art DWDM optical systems can span thousands of kilometers at 10 Gbit/s, and several hundred kilometers at 40 Gbit/s.

## Slide 7: Layer 1 – Physical Cables
Crossover Cables
  Used to connect similarly-pinned devices
  Auto-MDIX (Medium Dependent Interface Crossover) in Gigabit Ethernet makes crossover cables unnecessary

## Slide 8: Layer 1 – Physical Cables
Use straight-through cables for the following cabling:
Switch to router
  Switch to PC or server
  Hub to PC or server
Use crossover cables for the following cabling:
  Switch to switch
  Switch to hub
  Hub to hub
  Router to router
  PC to PC
  Router to PC

## Slide 9: Devices
Hubs – Layer 1
  Shared electrical bus
  All data copied to all ports
  Collisions occur when two systems try to talk at once
Switches – Layer 2
  Processes data to transmit only to the device for which the data was intended
  Systems connect at “full-duplex” w/o collisions

## Slide 10: Layer 2 – Ethernet LAN Addressing
Media Access Control (MAC)
  Unique identifier assigned to network interfaces for communications on the physical network segment
  6 bytes / 48bits long written in Hex
  (e.g. 01-23-45-67-89-ab or 01:23:45:67:89:ab )
  Source MAC stored in a table on the switch when a frame enters a port
  Forward, Filter, Flood
Notes: Forward on to the destination based on the MAC address table
Filter if the switch know there is nothing it should do with the frame
Flood out all ports if it know nothing about the destination host

## Slide 11: Devices
Routers/Multilayer Switches – Layer 3
  Device that forwards data packets between different computer networks based on IP address
  Uses routing protocol to learn routes
  Learned routes stored in a Routing Table

## Slide 12: Device Manufacturers
Dell/Force10
HP/3com
Cisco
Mellanox
IBM/BNT

## Slide 13: Layer 3 Addressing – IPv4
32-bit number written in dotted-decimal notation
  168.1.1.1 -> 1010100 00000001 00000001 00000001
  Each decimal number is called an octet…another term for byte
Broken up into “Classes”
Class A, B, and C are for hosts
Class D are multicast addresses
Class E are experimental

## Slide 14: Layer 3 Addressing – IPv4
All addresses in the same Class A, B or C network have the same numeric value for the network portion of the address…the rest of the address is call the host portion
Class A – 1-byte-long network part
Class B – 2-byte-long network part
Class C – 3-byte-long network part
Host portion loses two addresses for the Network address (first address) and Broadcast address (last address)

## Slide 15: Layer 3 Addressing – IPv4
Any Network of This Class | Number of Network Bytes (Bits) | Number of Host Bytes (Bits) | Number of Addresses per Network*
A | 1 (8) | 3 (24) | 224 – 2
B | 2 (16) | 2 (16) | 216 – 2
C | 3 (24) | 1 (8) | 28 – 2
*There are two reserved host addresses per network. |  |  | 
Sizes of Network and Host Parts of IP Addresses with No Subnetting

## Slide 16: Layer 3 Addressing – IPv4
List of All Possible Valid Network Numbers*
Class | First Octet Range | Valid Network Numbers* | Total Number of This Class of Network | Number of Hosts per Network
A | 1 to 126 | 1.0.0.0 to 126.0.0.0 | 27 – 2 = 126 | 224 – 2 = 16M
B | 128 to 191 | 128.1.0.0 to 191.254.0.0 | 214 – 2 = 16K | 216 – 2 = 65k
C | 192 to 223 | 192.0.1.0 to 223.255.254.0 | 221 – 2 = 2M | 28 – 2 = 254
*The Valid Network Numbers column shows actual network numbers. There are several reserved cases. For example, networks 0.0.0.0 (originally defined for use as a broadcast address) and 127.0.0.0 (still available for use as the loopback address) are reserved. Networks 128.0.0.0, 191.255.0.0, 192.0.0.0, and 223.255.255.0 also are reserved. |  |  |  | 

## Slide 17: Layer 3 - Subnetting
Splits up the massive Class networks into many smaller ones using Subnet Masks
Subnet masks perform a simple Boolean AND math operation
IP Address 8.8.0.4
Subnet Mask 255.255.0.0
00001000 00001000 00000000 00000100
11111111 11111111 00000000 00000000
Subnet = 8.8.0.0 /16 (Prefix notation)
Notes: 0 AND 0 = 0
0 AND 1 = 0
1 AND 0 = 0
1 AND 1 = 0
Prefix notation is another way to write the subnet mask. It is a slash followed by the number of consecutive 1’s in the binary representation of the subnet mask

## Slide 18: Layer 3 - Subnetting
Class A
IP Address 8.8.0.4 /16
Subnet Mask 255.255.0.0
00001000 00001000 00000000 00000100
11111111 11111111 00000000 00000000
NNNNNNNN SSSSSSSS HHHHHHHH HHHHHHHH
Number of Subnets = 2^S
Number of Hosts = (2^H) - 2

## Slide 19: Protocols
Spanning Tree Protocol
  Loop prevention by blocking some ports from forwarding frames
  DHCP issues
CDP/LLDP
  Good Layer 2 test
  Displays information about neighbor devices
    Chassis ID, Port ID, TTL, MAC

## Slide 20: Protocols
EtherChannel/LACP (Link Aggregation Control Protocol)
  Allows bonding of ports together to make logical bundles
  Load balanced by Source and/or Dest MAC or IP
  Etherchannel is Cisco Proprietary…bonded ports form a PortChannel
VLANS
  Create virtual switches to segment hosts into different networks
  Minimizes broadcast domains

## Slide 21: Cisco Three Tier Network Architecture
Core
Distribution
Access Layer