## Slide 1: CSCI 2930 Practical System Administration
Lecture 4: Desktops and Tier 1 Support (Continued)

## Slide 2: Desktop Components Video
Matrox
  Millennium
  G400/G450
  Environment Bump Mapping
  Professional 2D Graphics
  Multi Head Support
  Embedded Server Chips

## Slide 3: Desktop Components Video
3dFX
  First real 3D accelerators
  Voodoo PCI
  Pass-through
  Voodoo2 introduced Scan-Line Interleave (SLI) (Still required 2D card)
    Two Voodoo2 boards were connected together, each drawing half the scan lines of the screen

## Slide 4: Desktop Components Video
Nvidia
  Purchased 3dFX
  GeForce (Gaming)
  Quadro (Professional)
  Tesla (Compute)
  CUDA (Parallel/Programming – no Assembly)
  Reintroduced SLI (Scalable Link Interface)
AMD/ATI
  Radeon
  APU’s
  CrossFire

## Slide 5: Desktop Components Video
Intel
  Embedded chips on most lower-end mother boards
  Integrated on CPU’s
  MIC Compute (modified P54C)
    (Many Integrated Core)
    Larrabee
    Knights Ferry (Prototype)
    Knights Corner (22nm)
    Knights Landing (14nm)
    Xeon Phi (Product Family branding)
    Supercomputing

## Slide 6: Desktop Components Audio
Typically integrated onto the motherboard
  Line out
  Line In
  Rear/Center/Sub
  S/PDIF Out (OPTICAL)
  Microphone
Higher end boards provide 5.1 and 7.1 channels
Creative Labs de facto standard for discrete cards

## Slide 7: Desktop Components Local Storage
  PATA (IDE)
    Parallel ATA
    Integrated Drive Electronics
  SCSI
    Small Computer System Interface
  SATA
    Serial ATA
  SAS
    Serial Attached SCSI
  Discrete Cards
  RAID
    Redundant Array of Independent Disks

## Slide 8: Desktop Components Local Storage
  Parallel vs Serial
    Parallel can send multiple streams of data
    Able to clock Serial faster
    Less crosstalk with Serial
    Serial cables have less wires…take up less space
Notes: Parallel originally used because it was easier to push more data with multiple streams at slower bus speeds

## Slide 9: Desktop Components Hard Drives
Physical Sizes
  5.25”
  3.5”
  2.5”
  PCIe Cards
Media
  Magnetic
  SSD
  RAM

## Slide 10: Desktop Components Motherboard
CPU Socket
Main memory slots
North Bridge
South Bridge
Non-volatile memory BIOS/Firmware chips
Clock Generator
Expansion Card Slots
Power Connectors
Integrated devices
Battery
Voltage Regulator Module (VRM)
Notes: Show intel ark

## Slide 11: Desktop Components Motherboard
Form Factor
  AT
    Full
    Baby
  ATX
    Large number of sizes
    Airflow specifications
    Change in PSU connectors
    Power Supply Revisions

## Slide 12: Desktop Components Motherboard

## Slide 13: Desktop Components BIOS
Power-on-Self-Test POST
  Verify CPU registers
  Verify the integrity of the BIOS code itself
  Verify some basic components like DMA, timer, interrupt controller
  Find, size, and verify system main memory
  Initialize BIOS
  Pass control to other specialized BIOSes (if and when required)
  Identify, organize, and select which devices are available for booting

## Slide 14: Desktop Components BIOS
Features
  System clock
  Security
  Boot order
  Special features dictated by chipsets and processors
Flashing
  Separate boot environment
  Within OS
Backup Chips

## Slide 15: Desktop Components PSU
PSU
  Watts vs Amp
    The advent of high powered chips like the Opteron and P4 caused system builders to pay more attention to amps.
    May list high wattage but didn’t have enough amps on the power attached to the CPU
  Connectors
    4 pin molex
    SATA/SAS
    MB Power
    Floppy
    Graphics
    CPU

## Slide 16: Desktop Components PSU
Efficiency
  % of usable energy
  Saves Money
  Produces less heat

## Slide 17: Desktop Components Cooling
Thermal Design Point/Power (TDP)
Airflow
Fans
Heat Sinks
Heat Pipe
Liquid
Submersion
Peltier (Thermoelectric)
Notes: Liquid cooling is a highly effective method of removing excess heat, with the most common heat transfer fluid in desktop PCs being water. The advantages of water cooling over air cooling include water's higher specific heat capacity and thermal conductivity. The principle used in cooling computers is identical to that used in an automobile's internal combustion engine, with the water being circulated by a water pump through a block mounted on the CPU and out to a heat exchanger, typically a radiator.
A heat pipe is a hollow tube containing a heat transfer liquid. The liquid absorbs heat and evaporates at one end of the pipe. The vapor travels to the other (cooler) end of the tube, where it condenses, giving up its latent heat. The liquid returns to the hot end of the tube by gravity or capillary action and repeats the cycle.

## Slide 18: Desktop Components Cooling
Thermal Compound
  Fills air gaps between two surfaces with a thermally conductive substance
  Arctic Silver
Rounded Cables
Heat pockets
Notes: Liquid cooling is a highly effective method of removing excess heat, with the most common heat transfer fluid in desktop PCs being water. The advantages of water cooling over air cooling include water's higher specific heat capacity and thermal conductivity. The principle used in cooling computers is identical to that used in an automobile's internal combustion engine, with the water being circulated by a water pump through a block mounted on the CPU and out to a heat exchanger, typically a radiator.
A heat pipe is a hollow tube containing a heat transfer liquid. The liquid absorbs heat and evaporates at one end of the pipe. The vapor travels to the other (cooler) end of the tube, where it condenses, giving up its latent heat. The liquid returns to the hot end of the tube by gravity or capillary action and repeats the cycle.

## Slide 19: Desktop Components Optical Drives
Magneto Optical
  650MB to 9.2GB
CD-ROM/R/RW
  650MB
  700MB
DVD-+ROM/R/RW
  4.7GB – 9.4GB (Double Sided)
DVD-RAM
  Accessed like a hard drive similar to MO
  Higher Rewrite capacity and in hardware verification

## Slide 20: Desktop Components Optical Drives
Blu-ray (BD)
  25GB Single Sided
  50GB Double Sided
  100GB Three layer
  Hard Coat to protect against scratches
  Player Profiles based on features
Holographic
  300GB storage
  Companies continue to go bankrupt

## Slide 21: Desktop Components Cases
Form Factors
Materials
Fans
Controls
Connectors
PSU Location
Cable Management
Motherboard Mounting

## Slide 22: Monitors
CRT
LCD
  LED
Brightness/Contrast
Viewing Angles
Connections
  HDMI
  Display Port
  VGA
  DVI
Recycling

## Slide 23: Printers
Inkjet
  Create image by propelling droplets of ink onto paper
  Inkjet Heads
  Ink cartridges
Laser
  Beam projects an image of the page to be printed onto an electrically charged rotating drum
  Toner particles electrostatically picked up by the drum's charged areas
  Drum prints the image onto paper by direct contact and heat, which fuses the ink to the paper

## Slide 24: Printers
Multifunction
  Print
  Scan
  Fax
  Photocopy
Sharing
  Local printer shared out through OS specific protocols
  Built in Print Server
  Central server with multiple network printers

## Slide 25: Drivers
Translator between a hardware device and the applications or operating systems
Typical hardware devices that need special drivers:
  Printers
  Graphics Cards
  Network Cards
  Sound Cards
  Storage
  Cameras

## Slide 26: Warranty
Standard
Professional
Hours
  9 – 5
  24/7
  Weekdays Only
Response Time
  Depot Spares?
Apple

## Slide 27: Benchmarking
Assess the relative performance of an object by running a number of standard tests and trials
3DMark
  Graphics benchmark
PCmark
  PC component benchmark for home user workloads
LINPACK
  Linear Algebra
  Used for Top 500 super computer list
SiSoft Sandra
  Dhrystone (Integer)
  Whetstone (Floating Point)
FLOPS – Floating-point Operations Per Second

## Slide 28: Imaging/PXE
The Preboot eXecution Environment (PXE)
  Sometimes pronounced "pixie”
  Boot computer using a network interface
  Independent of data storage devices
Ghost - General Hardware-Oriented System Transfer
Kickstart
  Automatically perform unattended operating system installation and configuration
dd

## Slide 29: Lease vs Purchase
Lease
  + Equipment stays up-to-date
  + Predictable expenses
  - Pay more in the long term
Rotation
Recycling

## Slide 30: Helpdesk/Tickets
Software
Service Level Agreement (SLA)
Tier 1
  Support level responsible for basic customer issues
  Gather information and to determine the issue by analyzing the symptoms and figuring out the underlying problem
Tier 2
  Responsible for assisting Tier I solving basic technical problems and for
  Investigating elevated issues and seeking for known solutions related to these more complex issues

## Slide 31: Helpdesk/Tickets
Tier 3
  Experts in their fields
  Responsible for assisting both Tier I and Tier II
  Research and development of solutions to new or unknown issues
Priority
  End user priority v Helpdesk priority

## Slide 32: Helpdesk/Tickets
Example:
Feature | Support Included with Hardware Product Warranty | SupportEdge Standard | SupportEdge Premium
Storage System Installation | Not included but available for purchase | Not included but available for purchase | Included[*]
24x7 Remote Technical Support | Included | Included with hardware warranty | Included with hardware warranty
Target Response Objectives for Remote Technical Support | Not available | Priority 1: 2 hours Priority 2: 4 hours Priority 3: 16 hours Priority 4: 36 hours (all times on a 24x7 basis) | Priority 1: 30 minutes Priority 2: 2 hours Priority 3: 8 hours Priority 4; 24 hours (all times on a 24x7 basis)
Replacement Parts | Included | Included with hardware warranty | Included with hardware warranty
Replacement Parts Target Response Objectives and Installation | Next business day Customer installs all Replacement Parts. | Choose one of the following:[**] • 24x7, 4-hour (NetApp installs all Replacement Parts) • 24x7, 4-hour (Customer self-installs all Replacement Parts) • Next business day (NetApp installs all Replacement Parts) | NetApp installs all Replacement Parts. Choose one of the following:[**] • 24x7, 2-hour • 24x7, 4-hour • Next business day
Onsite Support | Not available | Not available | Included